## Slide 1
Chapter 2
Computer Network Technology
Chapter 2
Network Management: Principles and Practice
© Mani Subramanian 2000
2-1

## Slide 2
  Notes
Technology and Management
Chapter 2
What are the technologies that need to managed?
Challenges of technological progress on network management
Network Management: Principles and Practice
© Mani Subramanian 2000
2-2

## Slide 3
  Notes
Computer Network Technology
Chapter 2
Network comprises
  Nodes
  Links
Topology: How they’re configured
  LAN
  WAN
Distinction between LAN and WAN
Network Management: Principles and Practice
© Mani Subramanian 2000
2-3

## Slide 4
  Notes
LANs
Chapter 2
Type of LANs
  Ethernet
  Fast Ethernet
  Gigabit Ethernet
  Half-duplex Vs Full-duplex
  Switched Ethernet
  VLAN
  Token ring
  FDDI
  ATM / LANE
Network Management: Principles and Practice
© Mani Subramanian 2000
2-4

## Slide 5
  Notes
Nodes
Chapter 2
Hubs
Bridges
Remote bridges
Routers
Gateways
Half bridge / half router
Switches
Network Management: Principles and Practice
© Mani Subramanian 2000
2-5

## Slide 6
  Notes
WANs
Chapter 2
Facilities / Media
  Wired
    Copper
    Coaxial
    Fiber
  Wireless
    Terrestrial
    Satellite
Mode
  Digital
  Analog
Services
  POTS
  ISDN
  Broadband
Network Management: Principles and Practice
© Mani Subramanian 2000
2-6

## Slide 7
  Notes
Basic LAN Topologies
Chapter 2
Bus topology
  Used in Ethernet LAN family
  Common shared medium
  Randomized access (CSMA/CD)
  Easy to implement
  Lower utilization under heavy traffic 30%-40%
  Single culprit could effect the entire LAN
Network Management: Principles and Practice
© Mani Subramanian 2000
2-7

## Slide 8
  Notes
Basic LAN Topologies
Chapter 2
Ring Topology
  Used in token ring and FDDI
  Shared medium
  Deterministic access
  Master DTE has control
  High utilization >90%
Network Management: Principles and Practice
© Mani Subramanian 2000
2-8

## Slide 9
  Notes
Star & Hybrid LAN Topologies
Chapter 2
Star topology used with bus and ring topology
Hub is “LAN in a box”
What does the electronic LAN inside the box look like?
Why has hub become so popular?
Network Management: Principles and Practice
© Mani Subramanian 2000
2-9

## Slide 10
  Notes
A Campus Network
Chapter 2
ATM VLAN an alternative to FDDI backbone
Network Management: Principles and Practice
© Mani Subramanian 2000
2-10

## Slide 11
  Notes
WAN Topologies
Chapter 2
Mesh topology
  Implemented in network layer level
  Multiple paths between nodes
  Flat topology
  Redundancy
  Load balancing
  Shortest path
Tree topology
  Used with Ethernet bridges
  Hierarchical
  Efficient for small networks and special purpose networks
Network Management: Principles and Practice
© Mani Subramanian 2000
2-11

## Slide 12
  Notes
Ethernet
Chapter 2
IEEE 802.3 standard
10 Mbps data rate
Collision - analogy of hollow pipe
Principle of operation; CSMA/CD
Segment length and drop cable length
Minimum size of packet 64 bytes
Maximum size of packet 1500 bytes
Hub configuration
Network Management: Principles and Practice
© Mani Subramanian 2000
2-12

## Slide 13
  Notes
Fast Ethernet
Chapter 2
Rationale
  Max drop length 100m => Max round-trip time 1/10 of Ethernet; hence 10 times data rate
Standard 100Base-T4
Compatibility with 10BaseT
UTP limitation; Use 4-pair UTP @ 25 Mbps/pair
Alternatives: 2-pair 100BaseTX Cat 5(Max 100 m) and 100Base FX optical fiber (Max 2 km)
Hub
Station
4-pair UTP
Network Management: Principles and Practice
© Mani Subramanian 2000
2-13

## Slide 14
  Notes
LAN Data Rate Race
Chapter 2
E’Net
10Mbps
FDDI
100 Mbps
Fast E’Net
100Mbps
ATM
155.52 Mbps
Gbit E’Net
1 Gbps
Duplex
E’nets
ATM
OC-n
Network Management: Principles and Practice
© Mani Subramanian 2000
2-14

## Slide 15
  Notes
Gigbit Ethernet
Chapter 2
Packet size 512 bytes, slot size 4.096 microseconds
Minimum frame size 64 bytes for backward compatibility; Slot filled with carrier extension
Packet bursts with no idle time between frames increases efficiency
Network Management: Principles and Practice
© Mani Subramanian 2000
2-15

## Slide 16
  Notes
Switched Ethernet
Chapter 2
Maximum throughput increased ~N/2 in N-port hub
Snooping capability lost for management
Network Management: Principles and Practice
© Mani Subramanian 2000
2-16

## Slide 17
  Notes
Client/Server Configuration using
Switched Hub
Chapter 2
Network Management: Principles and Practice
© Mani Subramanian 2000
2-17

## Slide 18
  Notes
Virtual LAN
Chapter 2
Switched hub enables establishing virtual LANs
Permits switching stations between LANs without physical moving of equipment
Walk through scenario
Network Management: Principles and Practice
© Mani Subramanian 2000
2-18

## Slide 19
  Notes
Token Ring
Chapter 2
Adopted by IBM
IEEE 802.5 standard
Data rates of 4Mbps and 16 Mbps
Single and dual ring LANs
Network Management: Principles and Practice
© Mani Subramanian 2000
2-19

## Slide 20
  Notes
Dual Ring TR LAN
Chapter 2
Network Management: Principles and Practice
© Mani Subramanian 2000
2-20

## Slide 21
  Notes
Failure Recovery in TR LAN
Chapter 2
Station failure recovery
Link failure recovery
Network Management: Principles and Practice
© Mani Subramanian 2000
2-21

## Slide 22
  Notes
FDDI
Chapter 2
Uses fiber optics medium
Modified token ring protocol
Data rate 100 Mbps
Segment length 100 km
500 stations in the ring with max separation of 2 km
Single and dual attached stations
Dual attached stations load share the two rings
Network Management: Principles and Practice
© Mani Subramanian 2000
2-22

## Slide 23
  Notes
Basic Network Nodes
Chapter 2
Network Management: Principles and Practice
© Mani Subramanian 2000
2-23

## Slide 24
  Notes
Network Node Components
Chapter 2
Hubs
Bridges
Remote bridges
Routers
Gateways
Half bridge / half router
Switches
Network Management: Principles and Practice
© Mani Subramanian 2000
2-24

## Slide 25
  Notes
Hubs
Chapter 2
Hub is a platform
Function dependent on what is housed
  LAN
  Switched LAN
  Bridge
Network Management: Principles and Practice
© Mani Subramanian 2000
2-25

## Slide 26
  Notes
Stacked Hubs
Chapter 2
Hub ports can be scaled up using stacked hubs
Stacked hub
  extend back plane
  connected as daisy chain
Network Management: Principles and Practice
© Mani Subramanian 2000
2-26

## Slide 27
  Notes
Bridges
Chapter 2
Bridge
Local Bridge
Remote Bridge
Simple
Multiport
Multiport
Multi-protocol
Bridges two nodes at data link control layer
  Ethernet: tree topology, transparent bridge
  Token ring:mesh topology, source routing bridge
Remote bridge uses WAN interface cards; same protocol used at both ends
Ethernet bridge is a learning bridge
Network Management: Principles and Practice
© Mani Subramanian 2000
2-27

## Slide 28
  Notes
Routers
Chapter 2
Routers operate at network layer
Routes packets between nodes of similar network protocols
Routing table used to route packets
DLC and Physical layers could be different under the same common network layer protocol
Network Management: Principles and Practice
© Mani Subramanian 2000
2-28

## Slide 29
  Notes
Gateway
Chapter 2
Gateway is router connecting two networks with dissimilar network protocols
Gateway does the protocol conversion at the network layer
Protocol converter does the conversion at the application layer
Network Management: Principles and Practice
© Mani Subramanian 2000
2-29

## Slide 30
  Notes
Tunneling
Chapter 2
Joe’s Mobile
Loc: Seattle
Sally
L.A
Home LAN
NY
Tunneling
Foreign
Agent
Tunneling is transmission of packets (via multiprotocol routers) by encapsulation
In Figure 2.24, packets are encapsulated and transmitted through X.25 network in a serial mode
In the mobile environment, Joe and his home agent in NY communicate Joe’s Seattle location to the foreign agent. His communication with Sally in LA is tunneled
Network Management: Principles and Practice
© Mani Subramanian 2000
2-30

## Slide 31
  Notes
Half-Bridge
Chapter 2
Half-bridge (also referred to as half-router) is point-to-point communication
Uses PPP protocol
Helps low-end users to communicate with ISP on dial-up link saving the expense of dedicated link
Router encapsulates packets in PPP frames and puts serial outputs to the bridge, and vice-versa
Network Management: Principles and Practice
© Mani Subramanian 2000
2-31

## Slide 32
  Notes
Switched Networks
Chapter 2
Switches are embedded in bridges and routers
Switched network used in WAN
Two types of switched networks
  Circuit-switched
  Packet-switched
    Datagram service
    Virtual circuit
Network Management: Principles and Practice
© Mani Subramanian 2000
2-32

## Slide 33
  Notes
Transmission Technology
Chapter 2
Transmission Technology
Medium
Mode
Wired
Wireless
LAN
WAN
Digital
Analog
LAN Mobile Satellite
Physical transport media
  UTP
  Coax
  Fiber
  Terrestrial wireless
  Satellite transmission
Network Management: Principles and Practice
© Mani Subramanian 2000
2-33

## Slide 34
  Notes
Transmission Modes
Chapter 2
Network Management: Principles and Practice
© Mani Subramanian 2000
2-34

## Slide 35
  Notes
Broadband Services
Chapter 2
Integrated services: Voice, video, and data
Narrow band ISDN (Integrated Services Digital Net.)
  Basic rate:2B + D (B channel 64 kbps and D channel 16 kbps
  Primary rate: 23B + D channels
Broadband (ISDN) Services uses ATM technology
  SONET (Synchronous Optical Network) or SDH (Synchronous Digital Hierarchy)
  Data rate OC-n
    OC-1 51.84 Mbps
    OC-3 155.52 Mbps
  Access technologies:
    HFC (Hybrid Fiber Coaxial) / Cable modem
    ADSL (Asymmetric Digital Subscriber Line)
Network Management: Principles and Practice
© Mani Subramanian 2000
2-35