## Slide 1
Chapter 1
Data Communications
and
NM Overview
Chapter 1
Network Management: Principles and Practice
© Mani Subramanian 2000
1-1

## Slide 2
  Notes
Outline
Chapter 1
Analogy of telephone network
Data and telecommunication network
Distributed computing environment
Internet
Protocols and standards
IT management
Network and system management
Current status and future of network management
Network Management: Principles and Practice
© Mani Subramanian 2000
1-2

## Slide 3
  Notes
Telephone Network
Chapter 1
Characteristics:
  Reliable - does what is expected of it
  Dependable - always there when you need it (remember 911?)
  Good quality (connection) - hearing each other well
Reasons:
  Good planning, design, and implementation
  Good operation and management of network
Network Management: Principles and Practice
© Mani Subramanian 2000
1-3

## Slide 4
  Notes
Telephone Network Model
Chapter 1
Notice the hierarchy of switches
Primary and secondary routes programmed
Automatic routing
Where is the most likely failure?
Use of Operations Systems to ensure QoS
Network Management: Principles and Practice
© Mani Subramanian 2000
1-4

## Slide 5
  Notes
Operations Systems / NOC
Chapter 1
Monitor telephone network parameters
  S/N ratio, transmission loss, call blockage, etc.
Real-time management of network
Trunk (logical entity between switches) maintenance system measures loss and S/N. Trunks not meeting QoS are removed before customer notices poor quality
Traffic measurement systems measure call blockage. Additional switch planned to keep the call blockage below acceptable level
Operations systems are distributed at central offices
Network management done centrally from Network Operations Center (NOC)
Network Management: Principles and Practice
© Mani Subramanian 2000
1-5

## Slide 6
  Notes
Data and Telecommunication Network
Chapter 1
Computer data is carried over long distance by telephone (telecommunication network)
Output of telephone is analog and output of computers is digital
Modem is used to “modulate” and “demodulate” computer data to analog format and back
Clear distinction between the two networks is getting fuzzier with modern multimedia networks
Network Management: Principles and Practice
© Mani Subramanian 2000
1-6

## Slide 7
  Notes
IBM SNA Architecture
Chapter 1
IBM System Network Architecture (SNA) is a major step in network architecture
SNA is based on multitude of (dumb) terminals accessing a mainframe host at a remote location
Network Management: Principles and Practice
© Mani Subramanian 2000
1-7

## Slide 8
  Notes
DCE with LAN
Chapter 1
DCE.. Distributed Computing Environment
Driving technologies for DCE:
  Desktop processor
  LAN
  LAN - WAN network
Network Management: Principles and Practice
© Mani Subramanian 2000
1-8

## Slide 9
  Notes
LAN-WAN Network
Chapter 1
Major impacts of DCE:
  No more monopolistic service provider
  No centralized IT controller
  Hosts doing specialized function
  Client/Server architecture formed the core of DCE network
Network Management: Principles and Practice
© Mani Subramanian 2000
1-9

## Slide 10
  Notes
Client/Server Model
Chapter 1
Post office analogy; clerk the server, and the customer the client
Client always initiates requests
Server always responds
Notice that control is handed over to the receiving entity.
Request
Response
Network Management: Principles and Practice
© Mani Subramanian 2000
1-10

## Slide 11
  Notes
Client/Server Examples
Chapter 1
Network Management: Principles and Practice
© Mani Subramanian 2000
1-11

## Slide 12
  Notes
TCP/IP Based Networks
Chapter 1
TCP/IP is a suite of protocols
Internet is based on TCP/IP
IP is Internet protocol at the network layer level
TCP is connection-oriented transport protocol and ensures end-to-end connection
UDP is connectionless transport protocol and provides datagram service
Internet e-mail and much of the network mgmt. messages are based on UDP/IP
ICMP part of TCP/IP suite
Network Management: Principles and Practice
© Mani Subramanian 2000
1-12

## Slide 13
  Notes
Internet Configuration
Chapter 1
Walk through the scenario of e-mail from Joe to Sally
Network Management: Principles and Practice
© Mani Subramanian 2000
1-13

## Slide 14
  Notes
Architecture, Protocols and Standards
Chapter 1
Communication architecture
  Modeling of communication systems, comprising
    functional components and
    operations interfaces between them
Communication protocols
  Operational procedures
    intra- and inter-modules
Communication standards
  Agreement between manufacturers on protocols of communication equipment on
    physical characteristics and
    operational procedures
Examples: (Students to call out)
Network Management: Principles and Practice
© Mani Subramanian 2000
1-14

## Slide 15
  Notes
Communication Architecture
Chapter 1
Inter-layer interface: user and service provider
Peer-layer protocol interface
Analogy of hearing-impaired student
Role of intermediate systems
Gateway: Router with protocol conversion as gateway to an autonomous network or subnet
Network Management: Principles and Practice
© Mani Subramanian 2000
1-15

## Slide 16
  Notes
OSI Reference Model
Chapter 1
Importance of the knowledge of layer structure in NM
Network Management: Principles and Practice
© Mani Subramanian 2000
1-16

## Slide 17
  Notes
OSI Layers and Services
Chapter 1
Importance of services offered by different layers and the protocol conversion at different layers in NM
Network Management: Principles and Practice
© Mani Subramanian 2000
1-17

## Slide 18
  Notes
PDU Communication Model
Chapter 1
What is the relevance of PDU model in NM?
Network Management: Principles and Practice
© Mani Subramanian 2000
1-18

## Slide 19
  Notes
Gateway
Chapter 1
cc:mail from a station in Novel IPX network to an Internet station with SMTP e-mail
Network Management: Principles and Practice
© Mani Subramanian 2000
1-19

## Slide 20
  Notes
SNA, OSI, and Internet
Chapter 1
Similarity between SNA and OSI
Simplicity of Internet; specifies only layers 3 and 4
Integrated application layers over Internet
Commonality of layers 1 and 2 - IEEE standard
Network Management: Principles and Practice
© Mani Subramanian 2000
1-20

## Slide 21
  Notes
Application Protocols
Chapter 1
Internet user OSI user
Telnet Virtual Terminal
File Transfer Protocol File Transfer Access & Mgmt
Simple Mail Transfer Message-oriented Text Protocol Interchange Standard
Simple Network Common Management Management Protocol Information Protocol
Network Management: Principles and Practice
© Mani Subramanian 2000
1-21

## Slide 22
  Notes
NM Case Histories
Chapter 1
The case of the Footprint
Case of the crashing bridge
Network Management: Principles and Practice
© Mani Subramanian 2000
1-22

## Slide 23
  Notes
Common Network Problems
Chapter 1
Loss of connectivity
Duplicate IP address
Intermittent problems
Network configuration issues
Non-problems
Performance problems
Network Management: Principles and Practice
© Mani Subramanian 2000
1-23

## Slide 24
  Notes
Challenges of IT Managers
Chapter 1
Reliability
Non-real time problems
Rapid technological advance
Managing client/server environment
Scalability
Troubleshooting tools and systems
Trouble prediction
Standardization of operations - NMS helps
Centralized management vs “sneaker-net”
Network Management: Principles and Practice
© Mani Subramanian 2000
1-24

## Slide 25
  Notes
Network Management
Chapter 1
OAM&P
  Operations
  Administration
  Maintenance
  Provisioning
Network Management: Principles and Practice
© Mani Subramanian 2000
1-25

## Slide 26
  Notes
NM Functional Flow Chart
Chapter 1
Network Management: Principles and Practice
© Mani Subramanian 2000
1-26

## Slide 27
  Notes
NM Components
Chapter 1
Network Management: Principles and Practice
© Mani Subramanian 2000
1-27

## Slide 28
  Notes
Interoperability
Chapter 1
Message exchange between NMSs managing different domains
Network Management: Principles and Practice
© Mani Subramanian 2000
1-28

## Slide 29
  Notes
Status and Future Trends
Chapter 1
Status:
  SNMP management
  Limited CMIP management
  Operations systems
  Polled systems
Future trends:
  Object-oriented approach
  Service and policy management
  Business management
  Web-based management
Network Management: Principles and Practice
© Mani Subramanian 2000
1-29