## Slide 1
Chapter 5
SNMPv1:
Communication and Functional Models
Network Management: Principles and Practice
© Mani Subramanian 2000
5-1
Chapter 5

## Slide 2
Notes
SNMP Architecture
Truly simple network management protocol
Five messages, three from manager and two from agent
Network Management: Principles and Practice
© Mani Subramanian 2000
5-2
Chapter 5

## Slide 3
Notes
SNMP Messages
Get-Request
Get-Next-Request
Set-Request
Get-Response
Trap
  Generic trap
  Specific trap
  Time stamp
Generic trap
  coldStart
  warmStart
  linkDown
  linkUp
  authenticationfailure
  egpNeighborLoss
  enterpriseSpecific
Specific trap
  for special measurements such as statistics
Time stamp: Time since last initialization
Network Management: Principles and Practice
© Mani Subramanian 2000
5-3
Chapter 5

## Slide 4
Notes
Administrative Model
Based on community profile and policy
SNMP Entities:
  SNMP application entities - Reside in management stations and network elements - Manager and agent
  SNMP protocol entities - Communication processes (PDU handlers) - Peer processes that support application entities
Network Management: Principles and Practice
© Mani Subramanian 2000
5-4
Chapter 5

## Slide 5
SNMP Community
Security in SNMPv1 is community-based
Authentication scheme in manager and agent
Community: Pairing of two application entities
Community name: String of octets
Two applications in the same community communicate with each other
Application could have multiple community names
Communication is not secured in SNMPv1 - no encryption
Network Management: Principles and Practice
© Mani Subramanian 2000
5-5
Notes
Chapter 5

## Slide 6
Community Profile
MIB view
  An agent is programmed to view only a subset of managed objects of a network element
Access mode
  Each community name is assigned an access mode:: read-only and read-write
Community profile: MIB view + access mode
Operations on an object determined by community profile and the access mode of the object
Total of four access privileges
Some objects, such as table and table entry are non-accessible
Network Management: Principles and Practice
© Mani Subramanian 2000
5-6
Notes
Chapter 5

## Slide 7
Notes
Administration Model
Administration model is SNMP access policy
SNMP community paired with SNMP community profile is SNMP access policy
Parameters:
Community / communities
Agent / Agents
Manager / managers
Network Management: Principles and Practice
© Mani Subramanian 2000
5-7
Chapter 5

## Slide 8
Notes
Access Policy
Manager manages Community 1 and 2 network components via Agents 1 and 2
Agent 1 has only view of Community Profile 1, e.g. Cisco components
Agent 2 has only view of Community Profile 2, e.g. 3Com components
Manager has total view of both Cisco and 3Com components
Network Management: Principles and Practice
© Mani Subramanian 2000
5-8
Chapter 5

## Slide 9
Notes
Generalized Administration Model
Manager 1 manages community 1, manager 2 community 2,and manager 3 (MoM) both communities 1 and 2
Network Management: Principles and Practice
© Mani Subramanian 2000
5-9
Chapter 5

## Slide 10
Notes
Proxy Access Policy
Proxy agent enables non-SNMP community elements to be managed by an SNMP manager.
An SNMP MIB is created to handle the non-SNMP objects
Network Management: Principles and Practice
© Mani Subramanian 2000
5-10
Chapter 5

## Slide 11
Protocol Entities
Protocol entities support application entities
Communication between remote peer processes
Message consists of
  Version identifier
  Community name
  Protocol Data Unit
Message encapsulated and transmitted
Network Management: Principles and Practice
© Mani Subramanian 2000
5-11
Notes
Chapter 5

## Slide 12
Get and Set PDU
PDU Types: enumerated INTEGER
VarBindList: multiple instances of VarBind pairs
Network Management: Principles and Practice
© Mani Subramanian 2000
5-12
Notes
Chapter 5

## Slide 13
Notes
Error in Response
Error Index: No. of VarBind that the first error occurred
Network Management: Principles and Practice
© Mani Subramanian 2000
5-13
Chapter 5

## Slide 14
Trap PDU
Enterprise and agent address pertain to the system generating the trap
Seven generic traps specified by enumerated INTEGER
Specific trap is a trap not covered by enterprise specific trap
time stamp indicates elapsed time since last re- initialization
Network Management: Principles and Practice
© Mani Subramanian 2000
5-14
Notes
Chapter 5

## Slide 15
SNMP Operations
Network Management: Principles and Practice
© Mani Subramanian 2000
5-15
Chapter 5

## Slide 16
MIB for Get-Next-Request
Network Management: Principles and Practice
© Mani Subramanian 2000
5-16
Notes
Chapter 5

## Slide 17
Notes
Lexicographic Order
Procedure for ordering:
  Start with leftmost digit as first position
  Before increasing the order in the first position, select the lowest digit in the second position
  Continue the process till the lowest digit in the last position is captured
  Increase the order in the last position until all the digits in the last position are captured
  Move back to the last but one position and repeat the process
  Continue advancing to the first position until all the numbers are ordered
Tree structure for the above process
Network Management: Principles and Practice
© Mani Subramanian 2000
5-17
Chapter 5

## Slide 18
MIB Lexicographic Order
A 3.1
B 3.2
T Z
E
1.1
1.2
2.1
2.2
Network Management: Principles and Practice
© Mani Subramanian 2000
5-18
Notes
Chapter 5

## Slide 19
A More Complex MIB Example
Network Management: Principles and Practice
© Mani Subramanian 2000
5-19
Notes
Chapter 5

## Slide 20
Get-Next-Request Operation
Network Management: Principles and Practice
© Mani Subramanian 2000
5-20
Chapter 5

## Slide 21
Get-Next-Request Operation
Network Management: Principles and Practice
© Mani Subramanian 2000
5-21
Chapter 5

## Slide 22
Sniffer Data
Network Management: Principles and Practice
© Mani Subramanian 2000
5-22
Chapter 5

## Slide 23
SNMP MIB
Note: Most of the MIB objects were not used and hence deprecated in SNMPv2
Network Management: Principles and Practice
© Mani Subramanian 2000
5-23
Chapter 5